## Slide 1: 32-Bit RISC Architecture Block Diagrams
R32V2020

## Slide 2: Simplified Block Diagram
Instruction Memory
Register File
ALU
Timing / Sequencer
Data Memory
Stack Memory
Peripherals

## Slide 3: Instruction Space Path
Instruction Memory
Program Counter (r7)
Timing / Sequencer
Instruction Decoder
32
32
Instr.
Addr
Clock

## Slide 4: Data Space Path
Data Memory
Data Address (r6)
Timing / Sequencer
Register File
32
32
Data
Addr
n
Selects
Clock

## Slide 5: Stack Space Path
Stack Memory
Stack Address (r4)
Timing / Sequencer
Register File
32
32
Stack Data
Addr
n
Selects
Clock

## Slide 6: Peripheral Space Path
Peripheral Memory
Peripheral Address (r5)
Timing / Sequencer
Register File
32
32
Instr.
Addr
n
Selects
Clock

## Slide 7: Register File Overview
32-bits wide
16 Registers
  8 General Purpose Registers
  (3) Registers fixed at 0, 1, and -1
  Condition Code Register
  Stack, Data, Instruction, Peripheral Address

## Slide 8: Register File Data Path
Instruction Ctr/Reg (r7)
Data Adr
Ctr/Reg (r6)
Peripheral Reg (r5)
Timing / Sequencer
Clock
Stack Adr Ctr/Reg (r4)
G.P. Regs (r8-r15)
Cond. Code Reg. (r3)
-1 Value
Reg (r2)
One Value Reg. (r1)
Zero Value Reg. (r0)
ALU
MUX_A
ALU
MUX_B
Register File Input Data Mux
Stack Space Data Out
32
Data Space Data Out
32
32
ALU
32
32
Stack Space
Data In
Data Space
Data In
To CCR
ALU_Out
Stack Address
Peripheral Address
Data Address
Instruction Addr
Perip Space Data Out

## Slide 9: Fixed Value Registers (r0-r2)
Fixed Value Regs.
(r0-r2)
Reset
Output
Clock
Set to fixed value at reset
  May be synthesized away by FPGA compiler
Read-only values
  r0=0, r1=1, r2=-1

## Slide 10: Condition Code Register (r3)
Cleared to all 0’s at reset
Stores condition flags from ALU operation
Outputs go to flow controller
Cond.
Code
Reg.
(r3)
Reset
Output
Clock
ALU_CCR

## Slide 11: Stack Address Counter/Register (r4)
Cleared to 0x0 at reset
Loadable Counter
  Load from Register File Input Mux
  Load/Increment/Decrement
    Increment/decrement used with Stack Push/Pull operations
Stack Address
Counter/ Register
(r4)
Reset
Output
Clock
R.F. In Mux
LD/INC/DEC

## Slide 12: Peripheral Address Register (r5)
Cleared to 0x0 at reset
Register loaded from
  Register File Input Mux
Peripheral Address
Reg (r5)
RF IN Mux
Peripheral Address
Reset
Clock

## Slide 13: Data Address Register/Counter (r6)
Cleared to 0x0 at reset
Loadable Counter
  Load from Register File Input Mux
  Load/Increment control used for sequential operations (auto-increment)
Data Address
Counter/ Register
(r6)
Reset
Output
Clock
R.F. In Mux
LD/INC

## Slide 14: Instruction Register/Counter (r7)
Instr. Address
Counter/ Register
(r7)
Reset
Output
Clock
R.F. In Mux
LD/INC
Cleared to 0x0 at reset
Loadable Counter
  Load from Register File Input Mux
  Load/Increment
    Increment normally used for operation

## Slide 15: General Purpose Registers
Eight (8) General Purpose Registers
32-bits wide

## Slide 16: ALU

## Slide 17: Timing/Sequencer