## Slide 1: R32V2020 32-bit RISC Processor in EP4CE6
Land Boards
2019-04-25

## Slide 2: Target Hardware - Low End Off-the-shelf EP4 FPGA card

## Slide 3: EP4 On-card Resources
Hardware that has already been tested with the Multicomp project
  Altera EP4CE6 FPGA – 50 MHz clock
  USB-Serial
  PS/2 keyboard
  VGA
  Keys, LEDs, Buzzer

## Slide 4: EP4 On-card Resources (cont’d)
Hardware not yet tested with Multicomp
  SDRAM
  4 digit, 7 segment display
  A/D
  IR receiver
  Serial EEPROM

## Slide 5: VHDL Peripherals (tested with Multicomp)
VGA (2/2/2 video mode)
  Memory Mapped character display (64x32)
  ANSI terminal (UART emulation) display (80x32)
PS/2 Interface (connector on card)
UART
  6850 ACIA (via USB-Serial interface)
Sound
  Various from buzzes to tones

## Slide 6: Resources in Altera EP4CE6
Cyclone IV lowest end part
Logic Elements (LEs) = 6276
Embedded Memory (1Kx9 blocks) = 30
These elements set the resource budgets

## Slide 7: Architecture Blocks
Register File
16 regs
32-bits
Instruction
RAM
xKx32
Data
RAM
xKx32
Stack
RAM
xKx32
8-bit
I/O
Ctrlr
VGA
PS/2 Keyboard
USB
ALU
Instruction
Decoder
UART
PS/2 Keyboard
VHDL
Code
Hard-
ware

## Slide 8: Register File
16 registers (r0-r15)
32-bits per register
Some registers are dedicated and some are general purpose
Most registers clear to zero at reset
Uses < 512 Logic Elements (LEs)
  Less than 10% of the available EP4 LEs

## Slide 9: Register File (Cont’d)
Some registers are dedicated some are Gen Purp
  r8-r15 = General Purpose registers (8)
  r0 = always 0 (read-only – stores won’t change value)
  r1 = always 1 (read-only – stores won’t change value)
  r2 = always all 1’s (0xffff)
  r3 = Condition Code
  r4 = Stack Address
  r5 = Peripheral Address
  r6 = Data Address
  r7 = Program Address (loadable or auto-increment)

## Slide 10: Separate Address Spaces
Four independent address spaces
    Instruction Space
    Peripheral Space
    Data Space
    Stack Space
  There is plenty of interconnect in the FPGA
  Reduces multiplexing
    All writes can be essentially posted (don’t block the CPU unless the bus is busy from the last write
      With internal SRAM, peripheral bus could be busy

## Slide 11: Instruction Space
On-chip Dual Port RAM
  Read-only from the CPU
  Writeable from physical loader conn.
32-bit instructions
  Fixed instruction length (not ever variable)
  Fields in consistent positions
16-bits of address in EP4 FPGA (extensible)
  Up to 64K instructions
  EP4CE6 has limited space

## Slide 12: Peripheral Space
Needs to work with current set of peripherals
  Memory Mapped Display
  Terminal
  UART
  Latches (LEDs, etc)
  Read buffers (Switches, etc)
Address/Data match current peripheral space
  16-bits of address
  8-bits of data
    Reads/writes use bottom 8 bits of src/dest
      Zero pad the rest of the bits when read

## Slide 13: Data Space
On-chip Dual Port RAM
  Read-Write from the CPU
  External Loader can write only
16-bits of address in EP4 FPGA (extensible)
  32 bits of data
  Up to 64K Long words of data
Use is strictly limited to moves between Data Address Space and Registers

## Slide 14: Stack Space
Uses On-chip RAM
16-bits of address is more than enough since there's limited space in internal RAM
32 bits of data
Subroutine calls need the stack pushed/pulled automatically
  Always Push/pull general purpose regs
Resources: Depends on stack depth

## Slide 15: Instruction Format
32-bits wide
  8-bit wide OpCode
  rX,rY,rZ
    rX op rY => rZ
    4-bit wide source1 register select
    4-bit wide source2 register select
    4-bit wide destination register select
  Immediate format
    4-bit wide source1 register select
    16-bit wide immediate

## Slide 16: Opcode
See Opcode table spreadsheet